## Slide 1: Embedded Software Programming
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.

## Slide 2
Course Information
Notes: ++ Over the past few years, I have designed several backscatter and beyond backscatter systems that precisely overcome these critical challenges that have limited the widespread deployment of backscatter on IoT devices.
++ The research vision that I have pursued and would like to pursue as a faculty member is to enable a massive deployment of IoT devices by bridging the energy asymmetry between sensing, computation and communication blocks by designing novel platforms and communication mechanisms. I am going to describe some of my research contributions next.

## Slide 3: How would the student’s performance be graded
Component | Weightage to Overall Grade
Project | 50 %
Student Seminar | 20 %
Term Paper | 30 %
The end-term assessment has been removed. No end term assessment.

## Slide 4: Course Project
Component | Weightage to Project
Problem Statement (Novelty) | 25 %
Project Report | 15 %
Presentation | 25 %
Execution | 35%
Enables students to learn programming embedded platforms by building an application. The expectation is that students will develop something substantial. It does not necessarily need to have research component
A number of platform available: ESP32, Raspberry Pi, MSP430, Backscatter, FPGAs, and many other. Talk to us! Reach out after lecture or office hours

## Slide 5: Platforms for Project

## Slide 6: Platforms for project work

## Slide 7: Platform for project work

## Slide 8: Platform for project work

## Slide 9: nRF52833 – Microcontroller on the Micro:bit v2
32-bit ARM Cortex-M4F microcontroller
  64 MHz core, 128 KB RAM, 512 KB Flash
  Floating point support
  2.4 GHz Radio: Bluetooth Low energy / 802.15.4
  Various peripherals
    ADC, PWM
    I2C, UART, SPI, USB
    RNG, 32-bit Timers, Watchdog, Temperature
    Up to 42 I/O pins

## Slide 10: Course projects examples – Open AI Whisper and Embedded microphones
Bring high accuracy speech recognition to embedded device?
Too power consume to perform locally
Record audio, transmit to computer (Open AI Whisper), send back translated audio to embedded device;
Latency considerations? Other Optimizations etc?
Notes: Why do the IoT platforms suffer from this energy challenge? To understand this, we investigate the architecture of the IoT device. We show this architecture in the figure on the slide. It consists of a series of stages that enable us to sense physical phenomena, process and transmit the sensor information through a transceiver such as ZigBee/BLE/LoRa.
This architecture has remained unchanged over the past two decades. We find that during this time, sensors have become exceeding efficient. Today, we find sensors such as an accelerometer or a temperature sensor consumes just a few tens of microwatts of power consumption. However, we find that rest of the architecture components that are shown in red colour remain significantly energy expensive. To understand the reason for this significant energy asymmetry, we look at the following slide.

## Slide 11: Course projects examples – TinyML and Sensors
Machine learning techniques with sensor data
Tensorflow Lite on Arduino could be used as a platform
Reduce noise? Improve accuracy? Sensor fusion
Notes: Why do the IoT platforms suffer from this energy challenge? To understand this, we investigate the architecture of the IoT device. We show this architecture in the figure on the slide. It consists of a series of stages that enable us to sense physical phenomena, process and transmit the sensor information through a transceiver such as ZigBee/BLE/LoRa.
This architecture has remained unchanged over the past two decades. We find that during this time, sensors have become exceeding efficient. Today, we find sensors such as an accelerometer or a temperature sensor consumes just a few tens of microwatts of power consumption. However, we find that rest of the architecture components that are shown in red colour remain significantly energy expensive. To understand the reason for this significant energy asymmetry, we look at the following slide.

## Slide 12: Course projects examples – Application using IoT platforms, sensors, actuators etc
12
Something interesting that uses sensor, IoT platforms, actuators
Notes: Why do the IoT platforms suffer from this energy challenge? To understand this, we investigate the architecture of the IoT device. We show this architecture in the figure on the slide. It consists of a series of stages that enable us to sense physical phenomena, process and transmit the sensor information through a transceiver such as ZigBee/BLE/LoRa.
This architecture has remained unchanged over the past two decades. We find that during this time, sensors have become exceeding efficient. Today, we find sensors such as an accelerometer or a temperature sensor consumes just a few tens of microwatts of power consumption. However, we find that rest of the architecture components that are shown in red colour remain significantly energy expensive. To understand the reason for this significant energy asymmetry, we look at the following slide.

## Slide 13: Important Deadlines
Event | Date
Lectures | Starting Week 1 (15th January)
Student seminar paper selection | End of recess week (10th March)
Finalising project statement | End of recess week (10th March)
Student seminars | Lectures from 18th March
Project presentation | 15th April 2024
Term paper submission | 19th April 2024
Project submission | 19th April 2024

## Slide 14: Roadmap of the lecture today
Let us recall what was covered in the last lecture
Sensors and actuators
Teardown of common devices
Interfacing actuators through DAC and PWM
Interfacing peripherals through busses, UART
Introduction to SPI
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 15: Four main tasks performed by an embedded device
Computation and Storage
Sensing and Actuation
Power
Management
Wireless Networking
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 16: Cars are all software and sensors
Electric cars have numerous sensors and microcontrollers
Various sensors that are used in cars include:
  Tracking location: GPS (global positioning system)
  Distance measurement: Ultrasonic sensors
  Terrain mapping: Lidar (light detection and ranging)
  Proximity sensing: radar
  Various forms of cameras
  Motion sensor: accelerometers
  …. And many more
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 17: So, what are sensors ?
They are an eyes and ears for an embedded device. They sense environment and help to understand the physical world. Sensor is an electronic component that measures a physical phenomenon.
What are the phenomenon that you would like to sense and measure?
  Temperature
  Humidity
  Acoustic
  Vital signs
  …….
Choice of sensor depends on the target embedded application
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 18: Different forms of sensing: Active vs Passive
Passive Sensing
Active Sensing
When we talk about embedded systems we focus on passive sensing. As It is much cheaper and at a lower energy consumption

## Slide 19: Sensors have become exceedingly energy-efficient
During past decades, sensors have become exceedingly energy-efficient
  E.g., Accelerometer, Temperature, Image Sensors: Few µW’s of power
  Mostly passive sensors in constrained wireless embedded devices

## Slide 20: Sensors transform phenomenon into electrical signals
How sensors convert physical phenomena into electrical signals, we refer to Ohm's Law, which states that Voltage (V) equals Current (I) times Resistance (R)
V (Voltage) = I (Current) X R (Resistance)
By altering one of the variables in Ohm’s law —Voltage (V), Current (I), or Resistance (R)—in response to changes in the phenomenon, a sensor generates an analog electrical signal that corresponds to that phenomenon.

## Slide 21: Material Resistivity and its Role in Sensing Phenomena
Resistivity is a fundamental property of materials that quantifies how strongly a material opposes the flow of electric current. This property, denoted as ρ, can change in response to various physical phenomena such as temperature, light exposure, or mechanical strain
The resistance (R) of a conductor is determined by its resistivity (ρ), its length (L), and its cross-sectional area (A) as described by the equation:

## Slide 22: Material Resistivity and its Role in Sensing Phenomena
Resistivity (ρ): Materials with higher resistivity create more resistance for the same length and area. Resistivity is sensitive to physical conditions;
  Temperature: Many conductors have higher resistivity at higher temperatures.
  Light: Some materials (like photoresistors) change their resistivity exposed to light.
  Strain: Materials known as strain gauges increase in resistivity when stretched.

## Slide 23: Temperature sensing using resistivity changes
Thermistor is a sensor which varies in resistance based on temperature
Advantages: They are cheap and easy to use. Low cost
Disadvantages: They have a non-linear transfer function
Chart: Temperature (C)

## Slide 24: Light sensing using resistive changes
Photocell changes resistance with light (non-linear)
Example:
10 kΩ when dark
1 kΩ when light

## Slide 25: Taking a step back: Microcontrollers are digital
Conventional and widely used architecture of embedded wireless platform
Up to this point, we have talked about translating physical phenomenon to analog electrical signal changes
How do we convert the analog signal into digital?
Do we need to do any processing before the conversion operation?
Notes: Why do the IoT platforms suffer from this energy challenge? To understand this, we investigate the architecture of the IoT device. We show this architecture in the figure on the slide. It consists of a series of stages that enable us to sense physical phenomena, process and transmit the sensor information through a transceiver such as ZigBee/BLE/LoRa.
This architecture has remained unchanged over the past two decades. We find that during this time, sensors have become exceeding efficient. Today, we find sensors such as an accelerometer or a temperature sensor consumes just a few tens of microwatts of power consumption. However, we find that rest of the architecture components that are shown in red colour remain significantly energy expensive. To understand the reason for this significant energy asymmetry, we look at the following slide.

## Slide 26: ADC: Bridging the analog and digital worlds
ADCs convert analog signals, which have a continuous range of values, into digital signals, which have discrete numerical representations. This is essential for digital devices to process real-world analog inputs
What are the various parameters of the ADC?
  Resolution: Determined by the number of bits the ADC uses to represent the analog value. More bits mean higher resolution and finer granularity in the output
  Sampling Rate: The frequency at which the ADC samples the analog signal. Higher sampling rates can capture more detail and are necessary to comply with the Nyquist theorem. It also means higher power consumption
  Accuracy: The closeness of the ADC's output to the true input value. It includes factors such as linearity, noise, and error rate
Notes: Why do the IoT platforms suffer from this energy challenge? To understand this, we investigate the architecture of the IoT device. We show this architecture in the figure on the slide. It consists of a series of stages that enable us to sense physical phenomena, process and transmit the sensor information through a transceiver such as ZigBee/BLE/LoRa.
This architecture has remained unchanged over the past two decades. We find that during this time, sensors have become exceeding efficient. Today, we find sensors such as an accelerometer or a temperature sensor consumes just a few tens of microwatts of power consumption. However, we find that rest of the architecture components that are shown in red colour remain significantly energy expensive. To understand the reason for this significant energy asymmetry, we look at the following slide.

## Slide 27: Beyond resistive changes sensing: Potential
Thermocouple generates a voltage based on temperature
This principal is also used to enable harvesting energy from heat energy

## Slide 28: Generating voltage via piezoelectric effect
Compression of the material generates a voltage
Various sources of compression:
  Air Pressure
  Acceleration
  Strain

## Slide 29: Beyond resistive changes sensing: Potential
Generate a change in voltage that changes based on force

## Slide 30: Motion sensing: accelerometers
Accelerometers usually measure in g’s
  Where 1 g equals acceleration due to Earth gravity
Determining distance from acceleration is possible
  But messy. Error is squared when integrating
  Needs careful filtering and is only accurate over short periods
  Often fills in gaps between GPS samples (or other localization systems)
Accelerometers also work as tilt sensors
  Constantly sensing pull of gravity

## Slide 31: Motion sensing: Inertial measurement unit (IMU)
IMUs (a.k.a 9 degree-of-freedom, 9DOF) track motion of a device
  Acceleration (X, Y, Z axes)
  Rotation (X, Y, Z axes)
  Magnetism (X, Y, Z axes)
  Sometimes 6DOF with Acceleration + one of the others
Intelligent sensing: combines multiple sensors, ADCs, and computation with a wired interface
  9 analog inputs would otherwise be too many
Can be used to track motion, determine transportation method
  Smartphones, Robotics, etc.

## Slide 32: Roadmap of the lecture today
Let us recall what was covered in the last lecture
Sensors and actuators
Teardown of common devices
Interfacing actuators through DAC and PWM
Interfacing peripherals through busses, UART
Introduction to SPI
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 33: Active sensing: Ultrasound sensor
Emits high frequency sound waves from sensor which bounces from objects that are present in the environment
Estimates distance, proximity by measuring time taken for sounds waves to bounce back and propagate back to the ultrasound device
Power consuming, though can be used on IoT devices
Common application: Robotics, obstacle detection, water level sensing

## Slide 34: Passive Infrared (PIR) sensor
Detect movement in the environment
  By detecting change in IR levels
Often come with plastic lens cover to improve field of view and range

## Slide 35: PIR sensors come in digital and analog forms
Digital includes a preconfigured comparator

## Slide 36: There are even more types of sensors
Environment: Pressure, Humidity, Air Velocity, Air Quality
Rotation: Gyroscope
Distance: Ultrasonic, Lidar, or Radar
Biometric: Pulse Oximeter, Heart Rate
Agricultural: Soil moisture

## Slide 37: What are actuators?
Actuator is an electronic component that modifies a physical quantity
  Light/LED
  Motor
  Speaker
  …….
Notes: First, we look at the computational elements, and these consist of a microcontroller or an FPGA. Today, we find that these computational elements consume at least one order of magnitude higher power consumption when compared to the commonly used sensors.
However, we also find that microcontrollers are increasingly becoming energy efficient. We investigate a typical microcontroller that has been used in sensor platforms over the past two decades. We find that energy efficiency has improved by almost two orders of magnitude. Some of the present-generation microcontrollers, such as Ambiq Apollo4 consume just 3 uA/MHz than 330 uA for MSP430 used on platforms such as TelOS B.
If the trend continues, we can expect the microcontrollers to catch up with the sensors and become energy-efficient. This significant improvement is that the digital components are increasing becoming efficient as they follow moore’s law.

## Slide 38: Light emitting diodes (LEDs)
Directional component: only allows current to flow one way
Shorter side is the negative one
  i.e. where current flows to
Larger metal component
inside of case or case flat spot is cathode or
negative (-) lead
Shorter wire is cathode or
negative (-) lead
Negative ( - ) lead
Schematic Symbol
Notes: Light Emitting Diodes (LEDs) are vital actuators for embedded and Internet of Things (IoT) devices. They provide a visual indication of the device's state and can also be used for debugging purposes. LEDs are directional components that allow current to flow in one direction only.
Typically, the cathode, where the current flows, is the shorter side of the LED. LEDs are an effective way to indicate the status of a device and provide feedback during the development and testing phase.
They are also commonly used in consumer electronics and lighting applications.

## Slide 39: RGB LEDs
Three different colors of LED in a single large diffuser
Short leads are negative ends
  One for each color
Long lead is common power
  Common anode
Combinations of LEDs give other colors
  Cyan, Yellow, Violet, White
https://cdn-shop.adafruit.com/datasheets/FLR-100WAS-RGB.pdf
Notes: A unique variant of LEDs is the RGB (Red, Green, Blue) LED, which allows for the emission of three different colors. The short leads are the negative end, and each color has its own separate wire. By combining signals on multiple wires, a range of colors can be produced. RGB LEDs provide a versatile and efficient solution for adding color to embedded and IoT devices, as well as for lighting applications. By controlling the intensity of each color, a wide range of hues and shades can be generated, making RGB LEDs ideal for applications where dynamic color changes are desired.

## Slide 40: Light sensing: LEDs?
LEDs can be used as photodiodes as well!
  Apply reverse voltage. Read in leak current as voltage across a resistor using ADC

## Slide 41: Actuators on Sensor Tags?

## Slide 42: Sensors on SensorTag (CC2650)

## Slide 43: Other sensing platforms
Earables (Earphones as sensor)

## Slide 44: Let’s look at some commonly used IoT devices
Notes: Backscatter communication actually help us overcome this limitation

## Slide 45: What’s inside Apple AirTag
Nordic Semiconductor nRF52832 Bluetooth low-energy SoC w/NFC controller
Notes: Backscatter communication actually help us overcome this limitation

## Slide 46: What’s inside Apple AirTag
Accelerometer: Bosch Sensortec BMA28x 3-axis accelerometer
SoC/Microcontroller: Nordic Semiconductor nRF52832 Bluetooth low-energy SoC w/NFC controller
Actuator: Speaker
And many other componets….
Notes: Backscatter communication actually help us overcome this limitation

## Slide 47: Let’s look at some commonly used IoT devices
Notes: Backscatter communication actually help us overcome this limitation

## Slide 48: Let’s look at some commonly used IoT devices
MediaTek MT3333 GPS SoC
Bosch Sensortec BHI160 Accelerometer/Gyroscope w/ Sensor Hub
STMicroelectronics LIS2DW12 MEMS 3-Axis Accelerometer
Fitbit FBT18SW ARM application processor
Notes: Backscatter communication actually help us overcome this limitation

## Slide 49: Let’s look at some commonly used IoT devices
Notes: Backscatter communication actually help us overcome this limitation

## Slide 50: Let’s look at some commonly used IoT devices
Actuator, very important: 85 dB horn for alarm
Freescale SCK60DN512VLL10 custom Kinetis K60 low-power 100 MHz MCU (Cortex based)
Silicon Labs EM357 Ember Zigbee SoC
Murata Type ZX 2.4 GHz Wi-Fi 802.11b/g/n module (with Broadcom BCM43362 chipset)
Notes: Backscatter communication actually help us overcome this limitation

## Slide 51: TraceTogether Token
Notes: Backscatter communication actually help us overcome this limitation

## Slide 52: Roadmap of the lecture today
Let us recall what was covered in the last lecture
Sensors and actuators
Teardown of common devices
Interfacing actuators through DAC and PWM
Interfacing peripherals through busses, UART
Introduction to SPI
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 53: Digital signals
Simplest form of I/O
Exist in two states:
  High (a.k.a. Set, a.k.a. 1)
  Low (a.k.a. Clear, a.k.a. 0)
Simpler to interact with
  Constrained to two voltages
  With quick transitions between the two
  No math for voltage level
    Either high or low

## Slide 54: General Purpose Input/Output (GPIO)
Read/write from/to external pins on the microcontroller
  Two possible values: high (1) or low (0)
Basic unit of operation for microcontrollers
  Allows them to interact with buttons and LEDs
  Every microcontroller has GPIO

## Slide 55: DAC applications
What do you use an analog output for?
  Audio output
    But it needs to be high quality (resolution and speed)
  Motors
    But only with a controller that actually drives them with enough current
  LED brightness

## Slide 56: Digital-to-Analog Converters
Generates an analog voltage
DACs are conceptually the inverse of ADCs
  Number of bits of resolution choose analog step size
  Frequency determines step duration

## Slide 57: High resolution versus high frequency
What role does each play in a DAC? Which is more important?
High resolution can accurately represent a voltage
High frequency can accurately represent a changing voltage
In practice:
  Need high enough resolution, then as high of frequency as possible

## Slide 58: DACs are not in all microcontrollers
Not rare, but not ubiquitous either
  Every microcontroller has GPIO
  Just about every microcontroller has an ADC
  Some microcontrollers have DACs
Reasons
  Use cases are uncommon (and might need very high quality)
    Many devices can be controller digitally
  Pulse-Width Modulation (PWM) can emulate usably analog signals

## Slide 59: Pulse-Width Modulation
Much easier to control high or low than an analog output
Idea: modify how long a signal is high within some switching frequency, a.k.a duty cycle
  On 50% of the time for half voltage
  On 10% of the time for tenth voltage
Duty cycle, not frequency!

## Slide 60: PWM to Analog Signal example

## Slide 61: Every microcontroller can do PWM
Not every microcontroller has a PWM peripheral
But every microcontroller has timers and digital outputs
But all that is need is a GPIO and a Timer (or two)
  Timer determines when to turn GPIO on and off
  Often can be automated in hardware rather than use interrupt handler

## Slide 62: PWM applications
Servos
  Duty cycle chooses angle
Motor controllers
  Duty cycle chooses current and therefore speed
LED brightness
  And “breathing” effect
Audio
  Can sound okay if frequency is high enough

## Slide 63: Roadmap of the lecture today
Let us recall what was covered in the last lecture
Sensors and actuators
Teardown of common devices
Interfacing actuators through DAC and PWM
Interfacing peripherals through busses, UART
Introduction to SPI
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 64: Connecting peripherals: wired or wireless
Wired
  Send digital signals across one or more wires
  Advantages: Reliable, Low energy, Often simpler topology
  Disadvantages: Physically limiting
Wireless
  Send digital signals across another medium (usually RF)
  Advantages: Physically flexible,
  Disadvantages: Unreliable, High energy, Usually broadcast

## Slide 65: Number of wires to carry signal
Serial interface
  Single wire
  Transmit data as a “series” of bits separated by time
  Cheaper, but slower to transmit
Parallel interface
  Multiple wires
  Transmit data across multiple “parallel” wires simultaneously
  More expensive, but faster to transmit
Transmitter
Transmitter

## Slide 66: Speed of communication for busses
Inherently limited by the speed of light
  Speed of electricity 50-99% of that
  29 cm (11.4 in) = 1 nanosecond
Speed of communication is also limited by interference
  Faster the signals, the harder they are to distinguish
  More susceptible to interference (matters less for wired communication)
Limited by whether other device can keep up

## Slide 67: Example communication speed for wired protocol
Internal to platform, low-energy communication
  UART, 1-1000 kbps
  I2C, 100-400 kbps
  SPI, 1-100 Mbps
External (mostly serial) communication
  USB, 1-10000 Mbps
  Ethernet, 1-1000 Mbps
  HDMI, 4-48 Gbps
Internal parallel communication (less applicable to IoT devices)
  PCI, 8-32 Gbps
  RAM, 12-25 Gbps
Note: Speeds are measured in bit per second

## Slide 68: Controlling timing in wired communication
Synchronous communication
  Clock signal sent along with data
  Data is captured at edge of clock signal (rising or falling)
  Advantage: send signals very fast
  Disadvantage: extra pin and wire
Asynchronous communication
  Agree upon timing in advance and read data at that rate
  Advantage: no need for clock signal
  Disadvantage: clock synchronization
DATA
CLK
Transmitter
Receiver
b0
b1
b2
b3
b4
b5
b7
b6
D0
D1
D2
D3
D4
D5
D6
D7
CLK
Transmitter
Receiver
b0
b0
b0
b0
b0
b0
b1
b2
b3
b4
b5
b6
b7

## Slide 69: How to connect: point-to-point networks
How do we connect computers in a network?
  This is a question of “network topology”
  Simple option: just connect them directly
Problem: what if I find a third computer?

## Slide 70: How to connect: bus networks
Connect everything to one wire in parallel
  Scales well to many computers
Problem: which computer gets to transmit when?
  Simultaneous transmissions conflict
  Need a scheme for “arbitration”, deciding who transmits when

## Slide 71: How to connect: ring networks
Connect everything with point-to-point connections
  Connect the last computer back to the first computer
  Also known as Daisy-Chain (without the last connection back to the start)
Problem: what if a computer stops sending?

## Slide 72: How to connect: star networks
Connect to a hub with point-to-point connections
  Hub connects all computers
  Hub is a computer with one job: transfer communications between computers

## Slide 73: Microcontrollers often adopt star networks

## Slide 74: Universal Asynchronous Receiver Transmitter
Serial communication between two devices
Two wires: transmit and receive
Simple to implement and very common on microcontrollers
Tradeoff choices: Serial, Low speed, Asynchronous, Point-to-Point
Most frequently used to send text data between devices
  Microcontroller printf() output
  Radio AT commands to/from microcontroller

## Slide 75: Data frame for UART protocol
Signal is high by default
Goes low to trigger Start
Send each data bit (high=1, low=0), plus optionally parity bit
Goes high to trigger Stop

## Slide 76: UART example, transmitting 0x32 and 0x3C

## Slide 77: Baud rate for UART communication
Baud rate is a measure of “symbols per second”
  Typically 1 bit per symbol, but not always
  UART is 1 bit per symbol, but 8 data bits per 10/11 symbols
Any baud rate is possible
  But there are a handful of normal configurations
  115200 and 9600 are common

## Slide 78: UART sampling rate
How do we make asynchronous communication work?
  Both sides must agree on the baud rate
  Listen for start bit
  Conceptually:
    Only need to sample 9-10 more times at baud rate spacing
    Short enough that clocks should diverge too much
  Realistically:
    Sample 8 or 16 times per bit
    Determine boundaries between bits
    Select most common value between boundaries

## Slide 79: UART: chip-to-chip communication
Usually implemented as a two-wire interface
  TXD: Transmits data
  RXD: Receives data
  Optionally two additional pins for flow control
  No clock signal! Asynchronous
Note: TX connects to RX

## Slide 80: Detecting errors with parity
Choose one configuration for all UART messages
  Even parity: total number of “1” bits in data is even
  Odd parity: total number of “1” bits in data is odd
Parity bit: set to 1 or 0 to guarantee the parity configuration
  If message doesn’t match parity configuration at receiver, there was a bit error (single error detecting)
Example: Data = 10101011 (five “1” bits)
  Odd parity: set parity bit to zero
  Even parity: set parity bit to one

## Slide 81: What are error conditions for UART?
Parity failure
  Bit error when receiving data
Overrun
  New data arrived and overwrote buffer in peripheral before it was read
Framing
  Did not see Stop Bit when expected (should be guaranteed “1”)
Break condition
  Signal is low for entire message (Zero data plus Framing Error)
  Often used as a signal between devices

## Slide 82: Flow control for databits
How do we ensure that the other device is ready for the message?
  Add two pins for “hardware flow control”
  Ready To Send (RTS) output, signals that you want to send data
  Clear to Send (CTS) input, signals that other device is ready to receive
Software flow control is possible
  Send special byte that means pause or resume transmissions

## Slide 83: How to allow UART to communicate to computer?
FTDI makes the most common chip to do this (FT232)
Microbit uses a microcontroller to do this!
  KL27Z connects to USB
  Also connects to nRF52833 via UART and JTAG
  ttyACM0 is a “virtual serial device” on top of USB, miniterm is a serial console

## Slide 84: UART Pros and Cons
Pros
  Only uses two wires
  No clock signal is necessary
  Can do error detection with parity bit
Cons
  Data frame is limited to 8 bits (20% signaling overhead)
  Doesn’t support multiple device interactions (point-to-point only)
  Relatively slow to ensure proper reception

## Slide 85: boards/microbit_v2/microbit_retarget.c
printf() eventually calls _write()with formatted data
Converts stdio calls into UART TX and RX
Library just sets DMA and starts Tx

## Slide 86: Roadmap of the lecture today
Let us recall what was covered in the last lecture
Sensors and actuators
Teardown of common devices
Interfacing actuators through DAC and PWM
Interfacing peripherals through busses, UART
Introduction to SPI
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 87: Synchronous communication with a single device
Microcontroller
Data Out Clock
Device 2
Device 1
Device 3
Data In Clock

## Slide 88: Want bi-directional communication, so three wires
Microcontroller
Data Out Data In Clock
Device 2
Device 1
Device 3
Data In Data Out Clock

## Slide 89: Wire signals to all devices to form a bus
Microcontroller
Data Out Data In Clock
Data In Data Out Clock
Device 2
Device 1
Device 3
Data In Data Out Clock
Data In Data Out Clock

## Slide 90: Communicating on a bus
How do you distinguish which device you are talking to?
Address for each device
GPIO pin for each device

## Slide 91: Communicating on a bus
How do you distinguish which device you are talking to?
Address for each device
  Devices must always listen and then discard messages that aren’t for them
  Need to define packet format so it’s clear where the address is
  Need a method for addressing devices
GPIO pin for each device
  Signal which device is being communicated with
  Only activates communication on transition of “select” line

## Slide 92: Separate chip select line for each device
Microcontroller
Data Out Data In Clock
(2) Chip Select
Chip Select
  (3) Chip Select
Device 2
Device 1
Device 3
Data In Data Out Clock
Chip Select
Data In Data Out Clock
Chip Select
Data In Data Out Clock
Chip Select

## Slide 93: Serial Peripheral Interface (SPI)
Serial, synchronous, bus communication protocol
Single controller with multiple peripherals
  Within a circuit board
High-speed communication
  Multiple Mbps
Microcontroller
Serial Data Out Serial Data In Serial Clock
Device 2
Device 1
Device 3
Serial Data In Serial Data Out Serial Clock
Serial Data In Serial Data Out Serial Clock
Serial Data In Serial Data Out Serial Clock

## Slide 94: Roadmap of the lecture today
Let us recall what was covered in the last lecture
Sensors and actuators
Teardown of common devices
Interfacing actuators through DAC and PWM
Interfacing peripherals through busses, UART
Introduction to SPI
Notes: Here is the roadmap of the major topics that I am going to cover during the presentation. We have already covered the exponential growth of the internet of things; next, I will talk about the critical energy challenge that can severely hinder this massive growth and preventing us from realising this immense economic value enabled by the IoT.

## Slide 95: Embedded Software Programming
Ambuj Varshney
ambujv@nus.edu.sg
Notes: ++ Thank you for inviting me to give this talk
++ In this talk, I will present a pathway that can enable us to make wireless embedded systems ubiquitous. I will describe my previous research efforts that tackle the critical challenges that limit the growth of wireless embedded systems. These are related to the growing energy asymmetry that exists between sensing, computation and communication blocks on these platforms.
++ Finally, I will conclude my talk by covering the research agenda that I would like to work on as a faculty member.